Chapter 35  Electric Circuits

  - A Battery and a Bulb 548

- Inv: – Light a bulb with a battery and a piece of wire

- make sure all trials are diagramed

- Need a complete path – a circuit

- Inv: Examine a flashlight

- RQ 559	1	2

  - Electric Circuits 549

- Use a switch to break a circuit

- Series circuit – single pathway

- Parallel circuit – branched pathway

- RQ 559	3

  - Series Circuits 550

- Current does not pile up – everywhere the same

- Electrons move from negative to positive

- Break in circuit stops the flow of energy

- Characteristics

- Single pathway means the current is everywhere the same.

- The current is resisted by the resistance which is:

- The current in the circuit is equal to

- Ohm’s law applies separately to each device

- Votage supplied equals the sum of the voltage drop across each electrical component.       ???

e.	RQ	559		4	5

  - Parallel Circuits 552

- each electrical device connected in parallel is connected to the same two points of an electrical circuit.

- Each lamp has its own path from one terminal of the battery to the other.

- A break in one path does not affect the other path – each device operates independently of the other devices

- Characteristics

- The voltage across each device is the same.

- Ohm’s law applies separately to each branch

- The total current is equal to the sum of the branches:

- Total resistance of a circuit is less than the minimum resistance of any branch.

e.	RQ 559		6	7	8

  - Schematic Diagrams 554

- resistance – zigzag line

- ideal resistanceless wire – solid line

- battery – long and short line (long is +, short is –

- switch – either open or closed

  - Combining Resistors in a Compound Circuit 555

- desire to know the equivalent resistance of a circuit

- equivalent resistor replaces the individual resistors

- find equivalent resistance using the rules for adding resistors in series and parallel

- Investigate problems in the text

- Investigate using Mark David’s Apple program

- RQ	560		9	10	11

  - Parallel Circuits and Overloading 557

- All appliances are connected in parallel. (exception – Christmas bulbs)

- More appliances ( more current as total resistance decreases

- Lines overloaded if carry more current than what is same

- Do-----go to Builder Square – get values for various size wires and extension cords.

- Fuses – Circuit breakers

- RQ	560		12	13	14	15