Energy Transmission vs the Electric Potential of the Source

You have a cabin in the woods. Needing some electrical energy, you are presented with the following two sources.

1.	You can use a 12 volt battery that can produce a current of 10 amps.

2.	You can use a 120 volt electric generator which produces a current of 1 amp.

Each source is connected to the cabin through a cable with a resistance of 1 ohm.

Which would you choose?

Calculate the following quantities for each electrical source in the space provided below to find the answer.

Analysis of Energy Supplied by a 12 volt battery or a 120 volt electric generator

12 volt battery	120 volt electric generator

Power Available

P = I * V  -  12 volts * 10 amps		P = I * V  -  120 volts * 1 amp

120 watts		120 watts

Voltage Drop Across Wire

V = I * R  =  10 amps * 1 ohm	V = I * R  =  1 amp * 1 ohm

10 volts	1 volt

Power Loss Across Wire

P = I2 * R  =  (10 amps)2 * 1 ohm		P = I2 * R  =  (1 amp)2 * 1 ohm

100 watts		1 watt

Power Available at the Cabin

Pavailable - Plost		Pavailable - Plost

120 watts – 100 watts		120 watts – 1 watt

20 watts		119 watts