Let's Make Some Music

The tempered musical scale is a scale with constant ratio of frequencies between successive notes. There are 12 intervals between one octave and the next. The ratio between frequencies is the 12th root of 2 or 1.05946.

To construct a tempered scale using thin wall (1/2 inch) conduit pipe, one uses a ratio between lengths that is the 24th root of 2 or 1.0293.

A length of 12 and 11/16 inch will vibrate at 1024 Hertz. With this as the beginning length, an octave was made. The pipes were supported by two rubber bands at 1/4 the pipe length from each end, The following table was prepared using the above information. The popes were cut with the hope that the frequency would be slightly lower than desired. One could then use a file to shorten the pipes to obtain the desired frequency. The resonating frequencies were determined using the Vernier Frequency Meter program.

| Desired Frequency (Hertz) 1024.0 1084.9 1149.4 1217.7 1290.2 1366.9 1448.2 1534.3 1625.5 1722.2 1824.6 1933.1 2048 | Note C C# or Db D D# or Eb E F F# or Gb G G# or Ab A A# or Bb B C | Pipe Length (cm) 32.23 31.31 30.42 29.56 28.71 27.90 27.10 26.33 25.58 24.85 24.15 23.46 22.79 | 1/4 Pipe Length (cm) 8.06 7.83 7.61 7.39 7.18 6.98 6.78 6.58 6.40 6.21 6.04 5.87 5.70 | Actual Frequency (Hertz) 1027 1097 1146 1216 1296 1366 1446 1515 1615 1725 1804 2024 |
| --- | --- | --- | --- | --- |

Small diameter rubber bands can be purchased at any stationary store. And if you so desire, one can build a wooden frame to hold the pipes.

As you can see, I was unable to get all the pipes cut as I would have liked. However, for $1.97, I can purchase a 10-foot length of 1/2 inch conduit and begin again.

I have found no source of information pertaining to the length of thin wall tubing and their resonating frequency. Any help would be appreciated.

This was first seen when presented at an Ohio Section Meeting of AAPT by Fred Gram of Cuyahoga Community College.