FIRST PRINCIPLES

To understand how sundials work we have to think both about the rotation of the Earth and its orbit around the Sun.

The Earth rotates about an axis through the North and South Poles, completing one revolution in 23 hrs 56 mins 4.1 seconds. All points on the Earth's surface complete one revolution in that time.

We need to understand why the length of day, which is 24 hours, is not the same as the time of one revolution.

The Earth is also orbiting about the Sun at a distance of roughly 150,000,000 km or 93,000,000 miles. In one year it makes a complete circuit and the plane in which it travels is called the 'PLANE OF THE ECLIPTIC'. The axis always remains pointing in the same direction.

We use the word 'noon' to describe the time each day when the Sun appears highest in the sky. All places on the same meridian have the same noon. At noon our meridian is the part of the Earth's surface which is directly facing the Sun.

We measure time on Earth from noon one day until noon the next day. This span of time is divided into 24 equal hours. Because the Earth has moved a further 365 th of its orbit during the 24 hours, it has to turn slightly more than one revolution in order to directly face the Sun again. In fact it takes an average 3 minutes 55.9 seconds each day to do this. This is why the length of a day is not the same as the time of rotation.

The equatorial plane is at right angles to the axis.

The points directly above the North and South Poles are known as THE CELESTIAL POLES. The Earth's axis remains parallel to itself throughout the day and throughout the year, but it does move in a huge, nearly circular, orbit about the Sun. You might therefore think that the celestial poles would appear to move against the backdrop of the stars during the year. However, the stars are so far away that the difference is not noticeable except to very precise instruments and so we can say that the celestial poles are fixed points in the sky.

It so happens that there is a fairly bright star close to the north celestial pole. It is called 'POLARIS' or 'THE POLE STAR' and for practical purposes we can say that it is at the celestial pole. In the southern hemisphere there is no such convenient star.

The Earth's axis is at right angles to the equatorial plane, but it is not at right angles to the plane of the ecliptic. There is an angle of 231 26' between them.

As the Earth orbits the Sun, its axis always points in the same direction. The light from the Sun falls on the Earth at a varying angle to the equatorial plane according the Earth's position in its orbit. From Earth we see the Sun cross the sky on a slightly different track each day.

In dealing with sundials it is best to take an 'Earth centered' viewpoint. We can regard ourselves as fixed and the rest of the universe as moving round us. The Sun then appears to orbit around the Earth in a gentle spiral which takes a year to complete. The Sun passes directly overhead at noon at a latitude which gradually changes with the seasons. All latitudes where the Sun passes directly overhead lie within a band either side of the Equator between 23' 26'N and 23' 26'S, the region known as the TROPICS.

From December 2 1 st to June 2 1 st the Sun appears to travel a little further north each day, crossing the Equator on March 2 1 st until on June 2 1 st it is directly overhead at 23o26'N, the TROPIC OF CANCER. Then it travels a little further south each day, crossing the Equator on September 21st until on December 21st it is again at the furthest South at 23o.26'S, the TROPIC OF CAPRICORN.

The latitude where it is directly overhead is called 'THE DECLINATION OF THE SUN' and 2 table for the year is given below.

DECLINATION OF THE SUN

These figures are given in degrees and tenths of a degree and are the average for the four years of the leap year cycle. For any particular year, the value may differ by up to 0.3 degrees, but these are accurate enough for most purposes.

7

The part of the sundial which casts the shadow is called the 'GNOMON'. This is a Greek word which means 'indicator' or 'inspector'. It is pronounced no-mon, with the stress on the no. If we point a gnomon at the Pole Star, then it will be parallel to the Earth's axis and will always remain at the same angle to the ecliptic. This is essential if we are to make a sundial which works throughout the year.

This diagram shows that any line pointing at the celestial pole makes an angle with the horizontal equal to the latitude where it is installed. This vital line is marked in blue on all the sundials in this collection.

A shadow has to fall on a surface in order to be visible and clearly the direction of slope of the receiving surface affects the direction of the shadow.

Taking the 'Earth centred' viewpoint, the Sun orbits the Earth once a day and so the shadow of the axis falling on the equatorial plane must rotate evenly through exactly 3600 in 24 hours or 15' each hour. It must rotate through one degree every four minutes.

A shadow falling on any other plane than one parallel to the equatorial will not turn at a constant rate. It will therefore need trigonometry or careful geometrical construction to plot exactly where the shadow will fall at a particular hour. However, as long as the gnomon points at the celestial pole, the shadow will reach those marks at exactly the same hour each day.

THE HOUR ANGLE (H)

Since I hour corresponds to a change of 15' in the direction of the shadow on the equatorial plane, we can convert time to angle and vice versa by multiplying or dividing by 15. We take noon as zero. Angles in the morning are negative and in the afternoon are positive.

THE FUNDAMENTAL SUNDIAL - THE EQUATORIAL

When set for your latitude and placed on a horizontal surface facing north, the gnomon points to the celestial pole. The receiving surface with the scale on it is then parallel to the equatorial plane. Notice that the divisions are equally spaced at the 'hour angles'. When the sun is north of the Equator in spring and summer, it will shine only on the upper surface. In autumn and winter it will shine only on the lower surface. The Sun is then south of the Equator.

Around the dates of March 21st and September 21st you will notice that when the model is set up correctly neither face is properly illuminated and that the gnomon does not cast a proper shadow. This is because the scale plane of an equatorial sundial is parallel to the Earth's equatorial plane. On those dates the Sun is crossing the sky in the equatorial plane and it shines on the edge of the card all day.

6

POLAR SUNDIALS

The scale plane of a polar sundial is parallel to the Earth's axis and when it is in use the upper and lower edges are east-west. The hour markings are a projection of the 15' hour angles of the equatorial dial on to the tangent to the circle. The radius of the circle is equal to the height of the gnomon above the plane. The measurements can be found by construction, but if a calculator with trigonometrical functions is available, then it is probably easier to calculate them. The formula is X = 40 tan H because the gnomon of the model is 40mm high. H is the hour angle in degrees.

HORIZONTAL SUNDIALS

Horizontal sundials are probably the most commonly seen because they so often make interesting features in parks and gardens. The gnomon must point to the celestial pole and therefore must make the angle of latitude with the horizontal.

The horizontal plane seems very important to us but, we must remember that the fundamental plane for sundials is the equatorial. Hence the equal divisions which the shadow casts on the equatorial plane are not equal when projected on to the horizontal. They must be calculated for each particular latitude and the sundial will only work accurately at that latitude.

Fortunately the calculation is not too difficult because at any given latitude the horizontal plane makes a constant angle with the equatorial plane. If the latitude is L, then the angle is 90-L, the co-latitude.

The angles X which the hour divisions make with the noon line are given by the formula tan X = Sin L tan H.

This table gives some results, but it is best to calculate them exactly for your own latitude.

Both models which incorporate a horizontal dial have used an approximation in the interests of simplicity. Instead of providing a whole series of dials, one for each latitude, there is one calculated for the latitude 52' to serve for latitudes 450-60o. There is also an alternative dial calculated for latitude 381 to serve for latitudes 30o-45o. This introduces a certain amount of error and you may prefer to draw exact dials for your latitude using the formula above.

THE SOLAR COMPASS

LEA

VERTICAL SUNDIALS

Sundials on public buildings are often of the vertical type because they can be seen and admired, but are not easily reached and 'improved' by idle hands. If the wall faces due south, then the dial is called a 'direct south vertical dial'. The vertical dial on the 'three-in-one' sundial is of this type when it is correctly set up on a horizontal surface.

The vertical plane is also a projection from the equatorial plane and so the hour divisions are not equal. Since it is not the same projection as for the horizontal dial the divisions are not the same either. However, there is a simple connection between them.

The formula to calculate the hour angles X is

tan X = Cos L tan H

There is no need to complete this table because the hour divisions for a vertical sundial at a certain latitude are the same as the divisions for a horizontal sundial at the co-latitude.

A vertical dial only works for the latitude it was calculated for and the Sun never shines on it for more than 12 hours a day because it passes behind the plane of the wall. Nor can it ever give a shadow above the horizontal 6-6 line unless you take it up a high mountain! It is possible to make a direct north vertical dial for a north wall, but it will only work in summer, and then only in the early morning and late evening.

Sundials can also be designed for a wall which does not face directly south or north. This will be necessary if the building already exists. The projection of the equal divisions of the equatorial plane on to the wall is then more complicated, but it can be done and there are books to help. You can easily recognise such dials by the fact that the '12' is not vertically ards and that it is not symmetrical.

TRACKING THE SUN ACROSS THE SKY

The suntracker is not a sundial and it does not tell the time, but it provides an interesting way of investigating the path of the Sun as it crosses the sky each day. It is very dangerous to look directly at the Sun and the suntracker allows you to measure its angle of elevation and bearing very easily and with complete safety.

If you place it on a horizontal surface and set it as explained on its base you can find the angle of elevation (often called 'the altitude') and the bearing (often called 'the azimuth') as frequently as you wish. These results can be recorded in many ways, but perhaps the best idea is to plot them on circular graph paper like the 'suntrace paper' provided. It is a good idea to photocopy or trace several copies before marking them.

Here are some results.

For places west of the			For places cast of the

standard meridian			standard meridian

+ 4 mins per degree			-4 mins per degree

SUNDIAL TIME AND CLOCK TIME

Sundials can tell the time perfectly, and so can watches and clocks. However, they seldom tell the same time because they are not measuring the same thing.

Sundials measure the 'local apparent time', which is based on noon at the local longitude. Local noon is when the Sun 'souths' or crosses the meridian. Note that a.m. means 'ante meridiem' or 'before the Sun crosses the meridian and p.m. means 'post meridiem' or ,after the Sun crosses the meridian. The longitude where the Sun is crossing the meridian moves steadily westwards at a rate of 15 degrees per hour. As an example, the city of Bristol has a longitude of 2o35'W. Local noon occurs 10 mins 20 seconds after local noon at Greenwich and so a sundial in Bristol always shows a time 10 mins 20 seconds earlier than a sundial in Greenwich.

Such differences in clock time would be very inconvenient and so everywhere in Britain uses the time based on the Greenwich meridian. A watch in Bristol says the same as a watch at Greenwich. When a sundial in Bristol shows 12-00, a watch in Bristol shows 12-10 and both are correct. To be able to convert between one type of time and the other we have to consider three different adjustments.

1. ADJUSTMENT FOR LONGITUDE

The world has been divided into 24 time zones, each based on the prime meridian at Greenwich. The time cylinder shows those zones. To make the longitude adjustment you need to know your own longitude and the longitude of the standard meridian for your time zone. Then you add or subtract 4 minutes per degree according to whether you are west or east of the standard meridian.

Only if you live exactly on one of the standard meridians do you not have to make this correction. Fortunately it always remains the same at a particular place.

11

2. ADJUSTMENT FOR SUMMER TIME

Most countries put their clocks forward in Summer. it makes the evenings lighter and can save considerable quantities of coal, oil, gas and electricity, lt is usually called 'Summer Time' or 'Daylight Saving Time', but really it is 'Electricity Saving Time'.

A sundial knows nothing of such tricks! So you must remember to add an hour to the sundial time during the period of 'Summer Time'.

3. ADJUSTMENT FOR THE EQUATION OF TIME

Because the Earth's orbit is not a perfect circle and because the axis is inclined to the plane of the ecliptic, the time from noon till noon varies a little, according to the time of year. It would be most inconvenient if clock time were to vary from day to day and so clock time is averaged over a complete year. This is called 'Mean Time'. The 'Equation of Time', which would better be called 'The Equalisation of Time' is the difference between the 'Real Sun' and the 'Mean Sun'. This is the third adjustment which has to be added to sundial time to give clock time.

The special EQUATION OF TIME CARD gives the values for the year and reminds you of the three adjustments.

TIME CONVERSION

The total of the three adjustments is called 'TODAY'S ADJUSTMENT' and allows us to convert between sundial time and clock time.

EXAMPLE I Lo-toft, England on May 24th The standard meridian of Lowestoft is the Greenwich meridian at Ono. The longitude of Lowestoft is 1o44'E = 1.7oE. It is 1.70 east of its standard meridian

1. Longitude adjustment at - 4 mins per degree, 		ADJUSTMENT = -6.8onins

2. Summer time applies. Add I hour.		ADJUSTMENT - - 60 rains

3. Equation of time on May 24th			3.3min 	ADJUSTMENT = - 3.3.mins

TODAY'S ADJUSTMENT = + 49.9 mi.,

At 12.00 sundial time a watch will show 12.50 p.m.

EXAMPLE 2 Tulsa, Oklahoma on Nov 15th. The standard meridian of Tulsa is 'Central' at 900W. The longitude of Tulsa is 95o58'W = 96.0oW~ It is 60 west of its standard meridian.

1. Longitude adjustment at + 4 mim, per degree. ADJUSTMENT = 1 24 mins

2. Summer time does not apply.		ADJUSTMENT = 0

3. Equation of time on Nov 15th - -15.6mins		ADJUSTMENT - - 15.6 mins

TODAY'S ADJUSTMENT - + 8.4 mins

I		At 12.00 sundial time a watch will show 12.08 p.m.

SUNDIAL TIME + TODAY'S ADJUSTMENT = CLOCK TIME

FINDING NORTH

Sundials only work if the gnomon points to the celestial pole. The correct angle of elevation for your latitude was set as each model was being made and so it is only necessary to point it exactly to the north. Here are three possible methods which you could use to establish accurate north-south lines.

METHOD 1. A MAGNETIC COMPASS

The instrument which most people immediately think of when they wish to find north is a magnetic compass. However, a magnetic compass points to magnetic north which is not the same as true north. The correcting angle is called 'THE MAGNETIC VARIATION and it slowly changes. To find what it is you will need to consult a large scale map. In the East of England in 1987, true north was about 4 degrees east of magnetic north and was decreasing at about a fifth of a degree a year.

A magnetic compass offers the advantage that you can establish a north-south line at any time of the day or night whether or not the Sun is shining. Make certain, however that there is no iron nearby or you may get some very misleading results!

METHOD 2. THE SOLAR COMPASS

This instrument has been designed to find north-south and so it is ideally suited for the purpose. Since you are going to use clock-time to set it, you must carefully make the adjustments described on pages 11 and 12.

The north-south line can be established at any time between 9.00 a.m. and 3.00 p.m. local apparent time, as long as the Sun is shining.

METHOD 3. THE SUNTRACKER

Merck

Dubhe

Centre the

Pole Star Ir

r a k

THE NOCTURNAL

This device makes use of three bright stars in the northern hemisphere to tell the time at night. Because the Pole Star seems to remain fixed and to act as the hub around which all the other stars turn, we can use it as the Centre of a giant celestial clock.

There is a very convenient line from the Pole Star to the two 'pointers' in the Plough called Dubhe and Merak. By measuring the angle this line makes in the sky, we can tell the time.

If the Earth were not moving around the Sun as it rotated, then the stars would be at the same position in the sky at the same time each night. However, the effect of the motion about the Sun means that we look out into space in a slightly different direction each night, and that we see the stars reach their position of the night before 3 minutes 55.9 seconds earlier. That is why we have to set the date on the nocturnal before reading off the time.

Here are two positions to practise on.

The time given by a nocturnal is the same local apparent time that a sundial gives during the day. You may wish to adjust it to give clock times using the same adjustments given on pages I I and 12.

If you have enjoyed making these models, then there are other books which may interest you. In particular, THE TARQUIN GLOBE and THE TARQUIN STAR-GLOBE, both of which contain models to cut out and make yourself and include a minibook and a stand. Tarquin books are available from Bookshops, Toy Shops, Art/Craft Shops and in case of difficulty directly by post from the publishers. For an up-to-date catalogue, please write to Tarquin Publications, Stradbroke, Diss, Norfolk IP21 5JP, England.

On Sept 5th the time is 8.30 p.m. On June 10th the time is 2.30 a.m.

On Feb 28th it is 7.30 p.m. On Dec 10th it is 1.00 a.m.