1.	Describe the magnetic field around a current-carrying wire.

2.	Indicate the direction of the force

on the current carrying wire shown

in the diagram.

3.	What four factors control the force that acts on a wire in a magnetic field?

4.	Two parallel wires carrying a current in the same direction are attracted to each other.  Why?

5.	How would the force on an electron compare with that on a proton moving at the same speed in the same magnetic field.  The mass of the electron is 9.1 x 10-31 kg, of the proton 1.7 x 10-27 kg.

6.	An electron in a T.V. picture tube is moving with a speed of 3.0 x 107 m/s in a direction perpendicular to the earth's magnetic field of strength 5.5 x 10-5 N/amp-m.

a.	What is the magnetic force on the electron?

b.	What is the acceleration due to this force?

a.	__________________

b.	__________________

7.	A wire 60 cm long is in a magnetic field of 0.4 N/amp-m [North].  The force acting on the wire is 1.8 N. If the angle between the wire and the direction of the magnetic field is N 20o East (both measurements are made in a horizontal plane), what is the current in the wire?

__________________

8.	Sketch the magnetic field lines around a single loop of wire.

9. List three things that impressed you as you studied this chapter.