Short Answers    Chapter 3  Projectile Motion

Review Questions – 39

- Only a vector quantity is specified by direction.

- Speed has no direction,  velocity has direction

- 20 km/hr

- The diagram represents the resultant.

- It has 4 sides, with 2 pairs of sides parallel to each other.

- Smaller (each is 0.707 times the vector length)

- There is no component of force in horizontal direction.

- No component of gravitational force exists in horizontal direction.

- Same – both under the influence of gravity.

- Both hit the ground at the same time.

- a. 5 m    b. No; vertical displacement below any line is  ½ at2

- Straight up for maximum height; about 45o for maximum range

- 20 m/s

- a. equal to 20 m/s     b. Yes, decreases

- The projectile would be called an earth satellite.

- Close to the earth – 8 km/s

- To be above air drag, which would decrease its speed.

Only the force of gravity acts on the satellite.

Plug and Chug – 40

- 150 km/hr

- 175 km/hr [N]

- 141.4 km/hr at 45o to either vector

- 70.07 for both horizontal and vertical component

- 5 units;  the same

- 5-hypotenuse,  3-opposite 37o,  4 is opposite 53o

- Horizontal-8 units,   Vertical-6 units

- Horizontal-6 units,   Vertical-8 units

- Vertical, 16 m/s,  horizontal,   12 m/s,   horizontal,  vertical

- 18,000 mi/hr

Think and Explain - 	41

- 1 unit

- Yes, the diagonal of a rectangle is larger than either side.

- At terminal speed – must be air resistance

- Same speed (velocity vectors for the car and the rain are equal in magnitude.

- Because your component along the road’s direction decreases

- Zero speed at the top, 100 m/s horizontal at the top.

- Depends on vertical component;  only vertical component deals with ‘g’

- Same

- Its curved trajectory matches the curve of earth’s surface

It falls beneath the location it would reach if gravity didn’t act.

Think and Solve – 42

- A. 10 km/hr, across 36.86o downstream   b. if boat speed is 8 km/hr – angle of across 48.6o upstream,  if boat speed is 10 km/hr, then angle of across 36.9o upstream.

- 200 m

- 5 m/s

- aim 1.25 m above target

- 30 m/s since ball takes 2 seconds to fall 20 m

- 250 m from car (125 m fall takes 5 seconds)