| Right Hand Rule Used to Determine the Direction of a Magnetic Field Around a Current Carrying Wire Grasp the wire with right hand with thumb pointing in the direction of the current. (Direction that the positive charges are moving). Direction of magnetic field is circular, pointing in the direction of the fingers of the right hand. | Right Hand Rule Used to Determine the Direction of the Current in a Coil or the Identification of the North and/or South Pole of a Current Carrying Coil. Grab the coil with either: the thumb of the right hand pointing towards the North pole of the coil, or the fingers of the right hand wrapped around the coil pointing in the direction of the current in the coil. Knowing one of the two, the second can be found. |
| --- | --- |
| Right Hand Rule Used to Determine the Direction of the Magnetic Force on a Current Carrying Wire in a Magnetic Field Point the fingers of the right hand in the direction of the magnetic field. While keeping the fingers of the right hand pointing in the direction of the magnet field, point the thumb of the right hand in the direction of the current in the wire. The palm of the right hand will then point in the direction of the magnetic force on the current carrying wire. | Left Hand Rule Used to Determine the Direction of the Induced Current in a Wire Being Moved by a Mechanical Force Place the palm of the left hand in the direction of the mechanical force applied to the wire. While keeping the palm of the left hand pointing in the direction of the mechanical force, orient the fingers of the left hand in the direction of the magnetic field. The left thumb of your left hand will point in the direction of the induced current. |