Honors Physics  Chapter  5  Test    51 points         Name ____________________________

1.	Upon traveling to Mars, you drop a small ball and find that it takes 4.3 seconds to fall 19 meters.

| a. What is the acceleration due to the gravity of mars? (4) |  | b. If you have a mass of 36 kg, what is your weight on mars? (3) |
| --- | --- | --- |

2.	A 3800 kg helicopter accelerates upward at 0.70 m/s2 while lifting a 1800 kg car.

| a. What is the lift force exerted by the air on the rotors? (4) |  | b. What is the tension in the cable that connects the car to the helicopter? (3) |
| --- | --- | --- |

3.	A 74 kg person is standing in an elevator on a set of spring scales calibrated in Newtons. Suppose the elevator accelerates downward at 5.5 m/s2. What will the reading on the scale be? (4)

| 4. Draw a free-body diagram for each mass on the diagram shown at the right. (5) a. Find the tension in the string. _________(3) b. Find the rate at which the masses will accelerate. ____________ (3) c. How far will each mass move in 3.2 seconds? ____________ (3) |  |  |
| --- | --- | --- |

5.	A 25 kg box is pulled across a level floor, where the coefficient of kinetic friction is 0.57. What horizontal force is required for an acceleration of 3.0 m/s2? __________ (4)

| 6. An artillery gun is fired so that its shell has a vertical component of velocity of 240 m/s and a horizontal component of 340 m/s. If the target is at the same level as the gun, and air friction is neglected, a. How long will the shell stay in the air? _______________ (4) |  | b. how far down-range will the shell hit the target? _______________ (3) c. What is the final velocity of the ball? (4) |
| --- | --- | --- |

7.	A 290 g ball on the end of a string is rotated in a horizontal circle of radius 4.3 m. The ball completes 10 rotations in 5.3 s. What is the centripetal force of the string on the ball? (4)